## Slide 1: Tweaks to configured state machine for publisher
New state for failed attempts to connect a receiver.
Explicitly show state change messages associated with reconfiguration of subscriptions
Configured subscription state exposed (separate from receiver state) exposed within YANG model
leaf configured-subscription-state {
valid { value 1
invalid { value 2
concluded { value 3
.-------.
| start |-.
'-------' |
create .---modify-----.----------------------------------.
| | | |
V V .-------. .-----. .---------.
.----[evaluate]--no--->|invalid|-delete->| end |<-delete-|concluded|
| '-------' '-----' '---------'
|----[evaluate]--no-. ^ ^ ^
| ^ | | | |
yes | '->unsupportable delete stop-time
| modify (subscription- (subscription- (subscription-
| | terminated) terminated) concluded)
| | | | |
| .---------------------------------------------------------------.
'-->| valid |
'---------------------------------------------------------------'
.----------------------------------------------------------------.
| subscription valid |
| .----------. .--------. |
| | receiver |------------------timeout->|receiver| |
| |connecting|<------------------reset---|timeout | |
| | |<-transport---. '--------' |
| '----------' loss,reset | |
| | | | |
| (subscription | | |
| started) .--------. | .---------. |
| '----->| | '----------------------| | |
| |receiver|-(subscription-suspended)-->|receiver | |
|(subscription-| active | |suspended| |
| modified) | |<-(subscription-resumed,----| | |
| '---->'--------' subscription-modified) '---------' |
'----------------------------------------------------------------'
Configured receiver state machine goes in here
Configured subscription state machine

## Slide 2: New action to reset a configured receiver
+--ro receivers
+--ro receiver* [address port]
+--ro address inet:host
+--ro port inet:port-number
+--ro pushed-notifications? yang:counter64
+--ro excluded-notifications? yang:counter64
+--ro status enumeration
+---x reset-receiver
+--ro output
+--ro time yang:date-and-time
This action is useful if “connecting” state has timed out. Or if receiver has somehow lost track of subscription without publisher noticing

## Slide 3: Other changes
“time-of-update” in YANG Push removed as redundant with eventTime (RFC-5277) or the time elements under discussion within notification-messages.
Streams all made leafref to streams container. Stream container now must be “rw”, as YANG doesn’t allow configured subscriptions to point to configuration false streams.
“patch-id” Now a sequential number, starting with value ‘1’ for each on-change update. This allows easy identification of loss. Number resets to ‘1’ once it passes ‘99999’
Containers for ‘periodic’ and ‘on-change’ explicitly in subscription model. This ensures that you don’t have to guess which it is. It also allows for extensibility to new trigger types.
QoS objects moved from YANG push to Subscribed-notifications